## Slide 1
Lecture 18: Customize AXI IP
ELEC 4511
Hardware Software Design

## Slide 2
Customize AXI IP
In last lecture, we wrote C code in SDK and used Xilinx AXI GPIO core to turn on and off LED. From that lecture, you would have already known AXI GPIO is a “Verilog module”. And the ARM processor controls the module via AXI bus.
This lecture, you will design your own IP to control the LED.

## Slide 3
Customize AXI IP
Create a new Project.

## Slide 4
Customize AXI IP
Project_name : AXI_led_controller

## Slide 5
Customize AXI IP
Choose RTL Project.

## Slide 6
Customize AXI IP
Click “Boards” and select “PYNQ-Z1”

## Slide 7
Customize AXI IP
Tools  Create and Package New IP

## Slide 8
Customize AXI IP
Click on ”Next” and select “Create a new AXI4 Peripheral”

## Slide 9
Customize AXI IP
Give your IP a name : led_controller

## Slide 10
Customize AXI IP
You can choose the default settings on this page. You may find out we choose 4 registers (32 bits for each). However, in our design, we will only use 1. You will see that later
Your version number should be 1.0, since it is your first time to design this led_controller

## Slide 11
Customize AXI IP
Choose “ Edit IP” and click “Finish”

## Slide 12
Customize AXI IP
Under Sources, you will find two .v files:
The led_controller_v1_1_S00_AXI.v file contains the AXI bus protocols and your customized design module(your led controller)
And the led_controller_v1_1.v is the top wrapper file of the above one.

## Slide 13
Customize AXI IP
Open led_controller_v1_1_S00_AXI.v file
At line 17, find “// Users to add ports here”.
Add the LEDs_out port here. This port will connect to the pins of LD3 ~ LD0

## Slide 14
Customize AXI IP
Then at the end of this file, around line 400, find “// Add user logic here”
In the future, you may instantiate your design module here and write your code in another .v file.
However, this time the led controller is a very simple design. So we will directly write the logic code here.

## Slide 15
Customize AXI IP
Slv_reg0 is one of the 4 registers you created in slide 10.
PS send/receive data throughout the slave registers on AXI bus. For this design, PS will only send “turn on” or “turn off” signals to LED controller. And LED controller will directly give “high” or “low” voltage to the pins (LD3 ~ LD0)
Then save the file and open “led_controller_v1_1.v ”. At line 17, you will find “users to add ports here”. Please add your LEDs_out port here/

## Slide 16
Customize AXI IP
At line 51, modify the original instantiation, since you have modified the led_controller_v1_1_S00_AXI.v . Then save this file

## Slide 17
Customize AXI IP
Now you need to update your IP. Click on Merge changes from Customization Parameters Wizard

## Slide 18
Customize AXI IP
Review and Package  Edit packaging setting

## Slide 19
Customize AXI IP

## Slide 20
Customize AXI IP
Click OK and then click re-package IP. Then click yes to close the project

## Slide 21
Customize AXI IP
Then create a block design as you did in previous lectures.

## Slide 22
Customize AXI IP
Add IP. Search and find your led_controller

## Slide 23
Customize AXI IP
LEDs_out will be an external port to the board. So here click on the LEDs_out and right click it. Choose “make external”

## Slide 24
Customize AXI IP
Then add Zynq ps IP and “Run Block Automation” and “Run Connection Automation”

## Slide 25
Customize AXI IP
Tools  Validate Design

## Slide 26
Customize AXI IP
Create HDL Wrapper

## Slide 27
Customize AXI IP
Add pins constraint file for LEDs

## Slide 28
Customize AXI IP
Create a new constraint file

## Slide 29
Customize AXI IP
Add pins constraint file for LEDs

## Slide 30
Customize AXI IP
Open the XDC file and copy and paste the followings to the file
##LEDs
set_property -dict { PACKAGE_PIN R14 IOSTANDARD LVCMOS33 } [get_ports { LEDs_out_0[0] }]; #IO_L6N_T0_VREF_34 Sch=LEDs_out_0[0]
set_property -dict { PACKAGE_PIN P14 IOSTANDARD LVCMOS33 } [get_ports { LEDs_out_0[1] }]; #IO_L6P_T0_34 Sch=LEDs_out_0[1]
set_property -dict { PACKAGE_PIN N16 IOSTANDARD LVCMOS33 } [get_ports { LEDs_out_0[2] }]; #IO_L21N_T3_DQS_AD14N_35 Sch=LEDs_out_0[2]
set_property -dict { PACKAGE_PIN M14 IOSTANDARD LVCMOS33 } [get_ports { LEDs_out_0[3] }]; #IO_L23P_T3_35 Sch=LEDs_out_0[3]

## Slide 31
Customize AXI IP
Generate Bitstream
File  Export Export Hardware (include bitstream)
File  Launch SDK
In SDK, File  New  Application Project

## Slide 32
Customize AXI IP
Create an empty C project

## Slide 33
Customize AXI IP
Generate a new C source File

## Slide 34
Customize AXI IP
Don’t forget to add .c after your file name.

## Slide 35
Customize AXI IP
#include "xparameters.h"
#include "xil_io.h"
#include "AXI_led_controller.h"
#include "xil_printf.h"
#define LED_BASE_ADDR XPAR_AXI_LED_CONTROLLER_0_S00_AXI_BASEADDR
#define LED_REG0 0
#define DELAY 50000000
int main()
{
int temp = 0;
int led_value = 0;
int i = 0;
xil_printf("led_controller ip test\r\n");
xil_printf("----------------------\r\n");
while(1)
{
/* write reg0 */
AXI_LED_CONTROLLER_mWriteReg(LED_BASE_ADDR,LED_REG0,led_value);
/* read reg0 */
temp = AXI_LED_CONTROLLER_mReadReg (LED_BASE_ADDR,LED_REG0);
/* show value */
xil_printf("led = %d",led_value);
xil_printf("\ttemp = %d\r\n",temp);
if(led_value < 15)
led_value++;
else
led_value = 0;
for(i=0;i<DELAY;i++);
}
}

## Slide 36
Customize AXI IP

## Slide 37
Customize AXI IP
Close SDK
Export Block Design

## Slide 38
Customize AXI IP
Export Bitstream File
Make sure the bitstream has the same name as the .tcl file

## Slide 39
Customize AXI IP
Copy the .bit and .tcl to your pynq board

## Slide 40
Customize AXI IP
Copy the .bit and .tcl to your pynq board:
First, connect your pynq board with your PC via Ethernet. (static IP). Don’t forget to move your jumper.
Type in \\192.168.2.99\xilinx in your File Explorer.
(reference:
https://pynq.readthedocs.io/en/v2.0/getting_started.html)

## Slide 41
Customize AXI IP
Copy the .bit and .tcl to pynq/overlays/led
(You may create a folder “led”)
Create a new python 3 notebook and type in the code